CET 420

HW Chapter 1

Name:______________________

- If the 68HC11 is operated in the expanded mode, the I/O Subsystem is ___________ (lost, maintained).

- A Microcontroller on a development board is typically configured for expanded mode (TRUE or FALSE)

- List the four modes selected by the MODA and MODB pins (Refer to HC11 Ref Man – only 2 functions are shown in the text).

- Which pins (pin number and name – assume a PLCC 52 package) are used to wire an external master clock to the 68HC11?

- Compute one E clock cycle if following crystals are connected to the 68HC11 (show your calculations).

  - 8MHz

  - 4MHz

- Which pin(s) and PORTS would be used for the following input types (assume a PLCC 52 Package):

  - Analog in

  - Time Functions

  - Communications