CET 420

HW Chapter 2

Name:______________________

- List the seven CPU registers in a MC68HC11 microcontroller and state the size, in bits, of each.

- Accumulator A is the ___________ (upper/lower) byte and accumulator B is the

_____________(upper/lower) byte of accumulator D.

- List the five status bits within the condition code register. Which is the most used and why?

- Only arithmetic operations affect the status of the Z Flag (True / False).

- Name the six addressing modes used in the MC68HC11.

- The immediate addressing mode is signified by what symbol?

- How many address locations are allotted for the direct addressing mode and where do these addresses reside in memory?

- Write a direct addressing mode instruction to load the contents of accumulator A with the data found in location $64.

- Write a immediate addressing mode instruction to load the contents of accumulator A with the value $64.

- The relative addressing mode is limited to what range?