CET 420

## Lab #10

# Input Capture / Sonar

Due: End of Lab

Procedure:

- Read http://www.acroname.com/robotics/info/articles/sonar/sonar.html paying special attention to the following sections:

  - Interfacing to Microcontrollers

  - Power Supply Issues

  - Precautions

- Create a program that will:

  - generate a sonar pulse

  - measure the number of counts from the pulse was sent until an echo was returned

  - display the number of counts (representing the time) as a BCD value (with cr/lf)

The program should loop continuously and have a “time out” (i.e. if the sonar pulse is not returned within 32.77mSec “FFFF” is displayed and the cycle repeats).

Interrupts are not required for this program.

- Test the accuracy of the sonar by graphing time (counts) vs distance (both theoretical and actual).

Submit via email:

  - ASM CODE

  - Flow chart

  - Graph in excel spreadsheet (for #3 above)

Optional Formal Lab Report

Lab 9 + 10 can be written up as a FORMAL lab report, this will then be averaged with the previous formal labs as a way to bring up your formal lab report average.