CET 420

Test #1

# Study Guide

Test will cover Introduction, Chp 1-3, 6 and Labs 1 and 2. Flowcharting and Algorithm Design will NOT be on this test.

- Introduction

  - Difference between a microprocessor and microcontroller.

  - What is BUFFALO?

- Chapter 1

  - General description of ports (p 17)

    - Port A – Timer Functions

    - Port B – Binary Output / Expanded mode Addressing

    - Port C – Binary I/O – Expanded mode Data/Addressing

    - Port D – Communications

    - Port E – Binary Input / Analog Input

  - Pin Functions

    - MODA / MODB

    - EXTAL / XTAL

    - E Clock

    - Reset

  - What is a port replacement unit?

  - What is the difference between internal registers (A,B,X,Y) and the 68HC11 control registers found at memory locations $1000-$103F?

  - Be able to calculate bus and clock speeds given the other one. Also be able to calculate the time of one clock cycle.

  - Explain the difference between single chip and expanded mode.

- Chapter 2

  - Be able to reproduce and explain figure 2.1 (Programmer’s Model)

  - Be able to explain what the various bits of the CCR indicate and how they get set (excluding Interrupt bits and Stop bit)

  - What is the stack pointer? How does the processor use it?

  - What is the program counter? How does the processor use it?

  - Name the addressing modes and describe how they work by giving examples.

- Chapter 3

  - Name and describe the 5 function groups (see http://ceetusm.com/~dkohn/cet420/section_3.1.doc )

  - Expect to be given SIMPLE ASM code and have to trace though it (like in lab 2 #1)

  - You will be given the op code sheets shown here http://ceetusm.com/~dkohn/cet420/op_codes.pdf )

- Chapter 6

  - Know the following BUFFALO COMMANDS

    - MM

    - MD

    - RD

    - ASM

    - T

    - G

    - Load T