EET 200

Lab #3

Draw the following schematic in Protel.

Name the database your initials-3.ddb (ie dk-3.ddb)

Name the schematic Power Supply.sch

In the title block:

- Title the drawing: Power Supply.

- Make the organization name your name.

For U1 use the PROTEL DOS SCHEMATIC LIBRARY (sub library: PROTEL DOS SCHEMATIC VOLTAGE REGULATOR, Part LM317T)

Keep all part numbers the same.

Replace the plug (PL) with SOURCE VOLTAGE (from Miscellaneous Devices library)

Use the BRIDGE symbol to draw the 4 diodes (and label the BRIDGE U2)

Use the port symbol for the +/- outputs.

You do NOT have to draw waveforms.

Go to http://ceetusm.com/~EET200/ to submit the .ddb file.

Part descriptions:

| S1 | SPST |  | U1 | LM317T |
| --- | --- | --- | --- | --- |
| F1 | 1Amp |  | U2 | W06G |
| R1 | 230Ω |  | D5 | LED Red |
| C1 | 3300uf |  | C2 | 0.1uF |
| R2 | 240Ω |  | R3 | 5K |
| C3 | 1uF 35v |  | T1 | 120v/16v |